*********************************************************************

Serial Command Functions:

*********************************************************************

The Expanded Command set allows process variables to

be printed or modified by serial port command.

Basic Command Set:

Command			  Function

#		Aborts current command or data entry

@@A		Calibrate A Interpolator Commands

@@B		Calibrate B Interpolator Commands

@@C		Calibration Commands

@@D		Select display parameters

@@P		Print Commands - once to serial TX

@@R		Run Command - Resets and starts counter

@@S		Stop Command - Stops counter

@@U		Update EEPROM Calibration Values

Expanded Command Set:

@@A		Calibrate A Interpolator Commands

@@Ac	Set Ch A Center Value (xxx HEX)

@@As		Set Ch A Span Value (xxx HEX)

@@Az	Set Ch A Zero Value	(xxx HEX)

@@B		Calibrate B Interpolator Commands

@@Bc		Set Ch B Center Value (xxx HEX)

@@Bs		Set Ch B Span Value (xxx HEX)

@@Bz		Set Ch B Zero Value	(xxx HEX)

@@C		Calibration Commands

@@Cb 	Set the SPBRG value (xx HEX)

@@Cd	Disable Autocal Mode, Manual Cal Only

@@Ce		Enable Autocal Mode

@@Cg	Set Interpolation Gain Value xxx HEX

@@Ci		Set Inverted TXD polarity for TTL comm

@@Cl		Enable Cal Offset Limiter

@@Cn	Set Normal TXD polarity for RS-232 comm

@@Co	Set the OSCTUNE value (xx HEX)

@@Cr		Reset Autocal Peak Setectors

@@Ct		Set Calibration Time in Samples (xxxx HEX)

@@Cp	Print Calibration Values, Gain, and Time in HEX

@@Cu	Disable Cal Offset Limiter

@@Cv	Set Cal Offset Limiter Variance  (x HEX)

@@D		Display parameters

@@Dc	Toggle Display Calibration Values in BCD

@@Dd	Toggle Display 10-Digit Time Delay in BCD

@@Di		Toggle Display Corrected Start and Stop in BCD

@@Dp	Toggle Display Peak Detector Values

@@Dr		Toggle Display Raw Interpolator Data in BCD

@@Ds		Toggle Display Status Digit

@@Dt		Toggle Display TIC Counter Data in BCD

@@Dv	Toggle Display Interpolated Value in BCD

@@P		Print parameters:

@@Pb		Print SPBRG value in HEX

@@Pc		Print Calibration Data in BCD

@@Pg		Print Interpolation Gain in BCD

@@Pi		Print Interpolator Data in BCD

@@Po		Print OSCTUNE value in HEX

@@Ps		Print Status Digit

@@Pt		Print Calibration Time in BCD